## Slide 1
ESP32
Wireless Data Transfer
Temporary Folder
Facial Recognition Algortihm
Time
Count
Temperature
Image
Identity
Image
Auto File Handler
Time
Count
Temperature
Local Database & Webserver
Website
Time
Count
Temperature
Image
Identity
IIS
Access Worldwide
System Architecture
Hardware
Sensors
Software
Output
Legend
PIR Sensor
Ultrasonic
Thermal Sensor
Camera
Notes: The system architecture begins at the hardware and the sensors.
Once the hardware outputs the count, temperature, image, and the time it was all taken at, it is then wirelessly transfer into a temporary folder in the database.
From there, a system handler was created after a First-in, First-out queue to consistently monitor the temporary folder where all the files will be transferred into. The system handler is capable of automatically applying the facial recognition algorithm to the image files and moving updating the data into the database.
Once in the database, a local IIS webserver will consistently run an HTML request once new files have been added and show directly to the website.
A website consisting of html, css, javascript, and php are port forwarded using an IIS to be accessible worldwide.
Here is a simple demonstration of all the software architecture working together:
Once the image and datafiles are dropped in the database, the system handler executes necessary instructions and saves them all to the database.
Afterwards, the webpage displays all the newly acquired data using a javascript and php html request which is all accessible worldwide, all just over a second

## Slide 2
ESP32
Ultrasonic
Camera
Thermal
Sensor
PIR Sensor
Motion Trigger
Travel Direction Algorithm
If temp > th temp
Capacity
Count
Temperature
Image
If ( motion == true ):
- run travel algorithm
- start thermal camera
if ( temp > th && comingIn()):
- camera -> take picture
- send count, temp, image to database
ESP 32